Chefmaster Double Sauce Warmer

Instruction Manual

Model

HED241 Double Sauce Warmer

Thank you for purchasing your Chefmaster Sauce Warmer. To make full use of the product please read this manual carefully before using the product and keep it safe for future reference.

Safety Tips

- If you find any damage when the product is unpacked, contact your Chefmaster supplier within 24 hours of receipt of goods

- Always position on a flat stable surface

- Repairs should always be carried out by a qualified technician

- Do not overfill this product, keep water below the maximum level

- Do not allow water to drop below the minimum level

- Do not move the warmer when it contains hot liquid

- Do not use the unit outside

- Do not carry when the warmer is hot

- Always switch off and unplug the unit before cleaning

- Move by holding the unit by the base

- Always store flat and do no place heavy object on top of the unit

- If the power cord becomes damaged it must be replaced by a qualified technician

- This product is not designed to be used by persons with reduced physical or mental capabilities, lack of experience or knowledge, unless they are given suitable supervision, this includes children.

Pack Contents

- 1 x Sauce Warmer

- 2 x Sauce Pot with Lid

Before Use

- Remove all packaging including all protective plastic, from your Chefmaster Sauce Warmer

- Position on a flat stable surface

- Fill with water to below the maximum level

- Plug your Chefmaster Sauce Warmer into the mains

- The Sauce Warmer will now be ready to turn on

Operation

- Place the sauce pots to the Sauce Warmer

- Ensure the sauce warmer is plugged in and the power is on

- Turn the thermostat dial(s) to the required setting

Cleaning & Maintenance

- Before cleaning disconnect the Sauce Warmer from the electricity supply

- The Sauce Warmer should be cleaned with a warm, damp cloth

- DO NOT submerge the Sauce Warmer in water or use water sprays to clean it

- Always clean your Chefmaster Sauce Warmer daily

- The sauce pots are dishwasher safe.  Ensure they are cleaned before first use

Troubleshooting

| Fault | Possible Cause | Solution |
| --- | --- | --- |
| The power indicator light is not on | The unit is not switched on The plug or lead are damaged The fuse has blown | Check the unit is plugged in and switched on Contact your Chefmaster distributor Replace the fuse |
| The unit is on, water is not heating | Thermostat is too low Check water level The heating element has failed | Adjust thermostat Add more water if necessary Contact your Chefmaster distributor |

Transportation and Storage

Please handle your Sauce Warmer with care to prevent any damage to the unit and internal parts. The Sauce Warmer should be stored somewhere which is ventilation and non-corrosive gas.

Do not store any flammable objects near the equipment.

Technical Information

HED241 – Chefmaster Double Sauce Warmer

Voltage ~230v 50/60Hz

Power 0.4Kw

Weight 8kg

Capacity of Sauce Pot: 6.5Litre

Dimensions 505 x 280 x 320mm

- Chefmaster Sauce Warmer is supplied with a 3 pin plug and lead with a 13 amp fuse

- Appliance must be earthed

- If in doubt contact a qualified electrician or your Chefmaster distributor

Disposal

Under WEEE regulations this product must not be disposed of as household waste. To prevent damage to the environment and humans this product must be disposed of in an approved and environmentally friendly recycling process. For more information on how to dispose of this correctly please contact your Chefmaster distributor or local authority responsible for waste disposal.

Compliance

All Chefmaster parts and products have under gone a stringent testing process to ensure that comply with all European standards and specifications.

All Chefmaster products carry the CE approval symbol.